## Slide 1: ARMv8 Architecture
Girish S Kumar

## Slide 2
ARMv8 is the first architecture series where 64 Bit instruction sets are introduced

## Slide 3: Architecture terms in v8
AArch64 the ARMv8-A 64-bit execution state, that uses 31 64-bit general purpose registers (R0-R30), and a 64-bit program counter (PC), stack pointer (SP), and exception link registers(ELR). Provides 32 128-bit registers for SIMD vector and scalar floating-point support (V0-V31). A64 instructions have a fixed length of 32 bits and are always little-endian.
AArch32 is the ARMv7-A 32-bit execution state, that uses 13 32-bit general purpose registers (R0-R12), a 32-bit program counter (PC), stack pointer (SP), and link register (LR). AArch32 execution state provides a choice of two instruction sets, A32 (ARM) and T32 (Thumb2). Operation in AArch32 state is compatible with ARMv7-A operation.
T32: 16-bit instructions are decompressed transparently to full 32-bit ARM instructions in real time without performance loss.Thumb-2 technology made Thumb a mixed (32- and 16-bit) length instruction set

## Slide 4: ARMv8
The A64 instruction set provides some significant performance benefits, larger register pool.
ARM Architecture Procedure Call Standard (AAPCS) provide a performance boost when you must pass more than four registers in a function call. On ARMv7, this would require using the stack, whereas in AArch64 up to eight parameters can be passed in registers.
Wider integer registers enable code that operates on 64-bit data to work more efficiently. A 32-bit processor might require several operations to perform an arithmetic operation on 64-bit data. A 64-bit processor might be able to perform the same task in a single operation, typically at the same speed required by the same processor to perform a 32-bit operation. Therefore, code that performs many 64-bit sized operations is significantly faster.
64-bit operation enables applications to use a larger virtual address space.
The larger virtual address space also enables memory-mapping larger files. This is the mapping of the file contents into the memory map of a thread. This can occur even though the physical RAM might not be large enough to contain the whole file.

## Slide 5
Large physical address
  This enables the processor to access beyond 4GB of physical memory.
64-bit virtual addressing
  This enables virtual memory beyond the 4GB limit. This is important for modern desktop and server software using memory mapped file I/O or sparse addressing.
Automatic event signaling
This enables power-efficient, high-performance spinlocks.
Larger register files
  Thirty-one 64-bit general-purpose registers increase performance and reduce stack use.
Efficient 64-bit immediate generation
  There is less need for literal pools.
Large PC-relative addressing range
A +/-4GB addressing range for efficient data addressing within shared libraries and position-independent executables.
Additional 16KB and 64KB translation granules
  This reduces Translation Lookaside Buffer (TLB) miss rates and depth of page walks.

## Slide 6
New exception model
  This reduces OS and hypervisor software complexity.
Efficient cache management
  User space cache operations improve dynamic code generation efficiency. Fast Data cache clear using a Data Cache Zero instruction.
Hardware-accelerated cryptography
  Provides 3× to 10× better software encryption performance. This is useful for small granule decryption and encryption too small to offload to a hardware accelerator efficiently, for example https.
Load-Acquire, Store-Release instructions
  Designed for C++11, C11, Java memory models. They improve performance of thread-safe code by eliminating explicit memory barrier instructions.
NEON double-precision floating-point advanced SIMD

## Slide 7
ARMv8 PRocessor
 | Processor | 
 | Cortex-A53 | Cortex-A57
Release date | Jul-14 | Jan-15
Typical clock speed | 2GHz on 28nm | 1.5 to 2.5 GHz on 20nm
Execution order | In-order | Out of order, speculative issue, superscalar
Cores | 1 to 4 | 1 to 4
Integer Peak throughput | 2.3MIPS/MHz | 4.1 to 4.76MIPS/MHz[a]
Floating-point Unit | Yes | Yes
Half-precision | Yes | Yes
Hardware Divide | Yes | Yes
Fused Multiply Accumulate | Yes | Yes
Pipeline stages | 8 | 15+
Return stack entries | 4 | 8
Generic Interrupt Controller | External | External
AMBA interface | 64-bit I/F AMBA 4 | 128-bit I/F AMBA 4
 | (Supports AMBA 4 and AMBA 5) | (Supports AMBA 4 and AMBA 5)
L1 Cache size (Instruction) | 8KB to 64 KB | 48KB
L1 Cache structure (Instruction) | 2-way set associative | 3-way set associative
L1 Cache size (Data) | 8KB to 64KB | 32KB
L1 Cache structure (Data) | 4-way set associative | 2-way set associative
L2 Cache | Optional | Integrated
L2 Cache size | 128KB to 2MB | 512KB to 2MB
L2 Cache structure | 16-way set associative | 16-way set associative

## Slide 8
64-Bit pointer and registers
Fixed length (32bit) instructions
Load/store architecture
Little endian (big endian possible)
31 general purpose registers and zero register
ARM v8 features High level

## Slide 9: New Features
Load-acquire and store-release atomics
Crypto (AES and SHA) instructions
AdvSIMD usable for general purpose float math
Larger PC-relative addressing and branching
  Literal pool access and most conditional branches are extended to ± 1MB, unconditional branches and calls to ±128MB
Non-temporal (cache skipping) load/store
Load/store of a non-contiguous pair of registers

## Slide 10: New extensions provided with v8 arch
Jazelle is a Java hardware/software accelerator: “ARM Jazelle DBX (Direct Bytecode eXecution) technology for direct bytecode execution of Java”. On Sofware side: Jazelle MobileVM is a complete JVM which is Multi-tasking, engineered to provide high performance multi-tasking in a very small memory footprint
Floating Point: for floating point operations
NEON: the ARM SIMD 128 bit (Single instruction, multiple data) engine and DSP the SIMD 32bit engine useful to make linear algebra operations
Cryptographic Extension is an extension of the SIMD support and operates on the vector register file. It provides instructions for the acceleration of encryption and decryption to support the following: AES, SHA1, SHA2-256.
Trust Zone: is a system-wide approach to security for a wide array of client and server computing platforms include payment protection technology, digital rights management, BYOD, and a host of secured enterprise solutions

## Slide 11: New extensions provided with v8 arch
Virtualization Extensions with the Large Physical Address Extension (LPAE) enable the efficient implementation of virtual machine hypervisors for ARM architecture compliant processors.
  The visualization extensions provide the basis for ARM architecture compliant processors to address the needs of both client and server devices for the partitioning and management of complex software environments into virtual machines.
  The Large Physical Address extension provides the means for each of the software environments to utilize efficiently the available physical memory when handling large amounts of data

## Slide 13: What is NEON SIMD
ARM NEON technology is an advanced SIMD (single instruction multiple data) architecture extension for the Arm Cortex-A series and Cortex-R52 processors.

## Slide 14: NEON Technology
NEON technology was introduced to the Armv7-A and Armv7-R profiles. It is also now an extension to the Armv8-A and Armv8-R profiles. NEON technology is intended to improve the multimedia user experience by accelerating audio and video encoding/decoding, user interface, 2D/3D graphics or gaming. NEON can also accelerate signal processing algorithms and functions to speed up applications such as audio and video processing, voice and facial recognition, computer vision and deep learning.

## Slide 15: One Step Deeper into NEON
The NEON technology is a packed SIMD architecture.
NEON registers are considered as vectors of elements of the same data type.
Multiple data types are supported by the technology.
 | Armv7-A/R | Armv8-A/R AArch32 | Armv8-A AArch64
Floating Point | 32-bit | 16-bit*/32-bit | 16-bit*/32-bit/64-bit
Integer | 8-bit/16-bit/32-bit | 8-bit/16-bit/32-bit/64-bit | 8-bit/16-bit/32-bit/64-bit
The following table describes data types as supported by the architecture version.

## Slide 16
Math functions | Signal processing functions | Image processing functions | Physics functions
Vector Add | Floating & Fixed Point | Image Resize | Collision Detection
Matrix Add | Complex-to-Complex FFT | Image Rotate | 
Vector Subtract | Floating & Fixed Point |  | 
Vector Subtract From | Real-to-Complex FFT |  | 
Matrix Subtract | FIR Filters |  | 
Vector Multiply | FIR Decimator |  | 
Vector Multiply-Accumulate | FIR Interpolator |  | 
Matrix Multiply | FIR Lattice Filters |  | 
Matrix Vector Multiply | FIR Sparse Filters |  | 
Vector Divide | IIR Lattice Filters |  | 
Vector Set |  |  | 
Vector Length |  |  | 
Vector Normalize |  |  | 
Vector Absolute Value |  |  | 
Vector Dot Product |  |  | 
Vector Cross Product |  |  | 
Matrix Determinant |  |  | 
Matrix Inverse |  |  | 
Matrix Transpose |  |  | 
Matrix Identity |  |  | 
What is so special about NEON

## Slide 17: What are NEON intrinsics
NEON intrinsics are function calls that the compiler replaces with an appropriate NEON instruction or sequence of NEON instructions.
Intrinsics provide almost as much control as writing assembly language, but leave the allocation of registers to the compiler, so that developers can focus on the algorithms.
It can also perform instruction scheduling to remove pipeline stalls for the specified target processor. This leads to more maintainable source code than using assembly language.
NEON Intrinsics is supported by Arm Compilers, gcc and LLVM.

## Slide 18: Example of a Neon Intrinsic
#include <arm_neon.h>
uint32x4_t double_elements(uint32x4_t input)
{
return(vaddq_u32(input, input));
}

## Slide 19: List of Neon Intrinsic
int8x8_t vadd_s8 (int8x8_t a, int8x8_t b)
int8x16_t vaddq_s8 (int8x16_t a, int8x16_t b)
int16x4_t vadd_s16 (int16x4_t a, int16x4_t b)
int16x8_t vaddq_s16 (int16x8_t a, int16x8_t b)
int32x2_t vadd_s32 (int32x2_t a, int32x2_t b)
int32x4_t vaddq_s32 (int32x4_t a, int32x4_t b)
int64x1_t vadd_s64 (int64x1_t a, int64x1_t b)
int64x2_t vaddq_s64 (int64x2_t a, int64x2_t b)
uint8x8_t vadd_u8 (uint8x8_t a, uint8x8_t b)
uint8x16_t vaddq_u8 (uint8x16_t a, uint8x16_t b)
uint16x4_t vadd_u16 (uint16x4_t a, uint16x4_t b)
uint16x8_t vaddq_u16 (uint16x8_t a, uint16x8_t b)
uint32x2_t vadd_u32 (uint32x2_t a, uint32x2_t b)
uint32x4_t vaddq_u32 (uint32x4_t a, uint32x4_t b)
uint64x1_t vadd_u64 (uint64x1_t a, uint64x1_t b)
uint64x2_t vaddq_u64 (uint64x2_t a, uint64x2_t b)

## Slide 20: List of Neon Intrinsic
float32x2_t vadd_f32 (float32x2_t a, float32x2_t b)
float32x4_t vaddq_f32 (float32x4_t a, float32x4_t b)
float64x1_t vadd_f64 (float64x1_t a, float64x1_t b)
float64x2_t vaddq_f64 (float64x2_t a, float64x2_t b)
int64_t vaddd_s64 (int64_t a, int64_t b)
uint64_t vaddd_u64 (uint64_t a, uint64_t b)
int16x8_t vaddl_s8 (int8x8_t a, int8x8_t b)
int32x4_t vaddl_s16 (int16x4_t a, int16x4_t b)
int64x2_t vaddl_s32 (int32x2_t a, int32x2_t b)
uint16x8_t vaddl_u8 (uint8x8_t a, uint8x8_t b)
https://developer.arm.com/technologies/neon/intrinsics

## Slide 21: Registers in ARMv8
The AArch64 execution state provides 31 × 64-bit general-purpose registers accessible at all times and in all Exception levels.
Each register is 64 bits wide and they are generally referred to as registers X0-X30.
X0 | W0
X1 | W1
X2 | W2
X3 | W3
X4 | W4
X5 | W5
X6 | W6
X7 | W7
X8 | W8
X9 | W9
X10 | W10
X11 | W11
X12 | W12
X13 | W13
X14 | W14
X15 | W15
X16 | W16
X17 | W17
X18 | W18
X19 | W19
X20 | W20
X21 | W21
X22 | W22
X23 | W23
X24 | W24
X25 | W25
X26 | W26
X27 | W27
X28 | W28
X29 | W29
X30 | W30
0
63
32
31
32 Bit
Wn
64 Bit
Xn

## Slide 22: Register Names and uses
r30 (LR): The Link Register, is used as the subroutine link register (LR) and stores the return address when Branch with Linkoperations are performed.
r29 (FP): The Frame Pointer
r19…r28: Callee-saved registers
r18: The Platform Register, if needed; otherwise a temporary register.
r17 (IP1): The second intra-procedure-call temporary register (can be used by call veneers and PLT code); at other times may be used as a temporary register.
r16 (IP0): The first intra-procedure-call scratch register (can be used by call veneers and PLT code); at other times may be used as a temporary register.
r9…r15: Temporary registers
r8: Indirect result location register
r0…r7: Parameter/result registers
The PC (program counter) has a limited access, only few instructions, as BL and ADL, can modify it

## Slide 23: Special Purpose Registers in v8
Name | Size | Description
WZR | 32 bits | Zero register
XZR | 64 bits | Zero register
WSP | 32 bits | Current stack pointer
SP | 64 bits | Current stack pointer
PC | 64 bits | Program counter

## Slide 24: Zero Register
Essentially, register 31 does not really exist and that value is used in certain instructions to encode a variety of things as a kind of shortcut.
In most data processing operations, it indicates a register which reads as zero and which ignores writes. This allows you to specify a constant value of zero easily anywhere you can use a valid register name and also to compose an instruction which discards its result. The assembler accepts WZR and XZR as a name for this "register".
The zero register reads as zero when used as a source register and discards the result when used as a destination register. You can use the zero register in most, but not all, instructions.

## Slide 25: Stack Pointer
In the ARMv8 architecture, the choice of stack pointer to use is separated to some extent from the Exception level. By default, taking an exception selects the stack pointer for the target Exception level, SP_ELn. For example, taking an exception to EL1 selects SP_EL1. Each Exception level has its own stack pointer, SP_EL0, SP_EL1, SP_EL2, and SP_EL3. When in AArch64 at an Exception level other than EL0, the processor can use either:
A dedicated 64-bit stack pointer associated with that Exception level (SP_ELn).
The stack pointer associated with EL0 (SP_EL0).
EL0 can only ever access SP_EL0.
The SP cannot be referenced by most instructions. However, some forms of arithmetic instructions, for example, the ADD instruction, can read and write to the current stack pointer to adjust the stack pointer in a function. For example:
ADD SP, SP, #0x10 // Adjust SP to be 0x10 bytes before its current value

## Slide 26: Program Counter
One feature of the original ARMv7 instruction set was the use of R15, the Program Counter (PC) as a general-purpose register. The PC enabled some clever programming tricks, but it introduced complications for compilers and the design of complex pipelines. Removing direct access to the PC in ARMv8 makes return prediction easier and simplifies the ABI specification.
The PC is never accessible as a named register. Its use is implicit in certain instructions such as PC-relative load and address generation. The PC cannot be specified as the destination of a data processing instruction or load instruction.

## Slide 27: Exception Link Register
The Exception Link Register holds the exception return address.

## Slide 28: Saved Process Status register
When taking an exception, the processor state is stored in the relevant Saved Program Status Register (SPSR), in a similar way to the CPSR in ARMv7. The SPSR holds the value of PSTATE before taking an exception and is used to restore the value of PSTATE when executing an exception return.
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
N | Z | C | V |  |  |  |  |  |  | SS | IL |  |  |  |  |  |  |  |  |  |  | D | A | I | F |  | M | M[3:0] |  |  | 

## Slide 29
N | Negative result (N flag).
Z | Zero result (Z) flag.
C | Carry out (C flag).
V | Overflow (V flag).
SS | Software Step. Indicates whether software step was enabled when an exception was taken.
IL | Illegal Execution State bit. Shows the value of PSTATE.IL immediately before the exception was taken.
D | Process state Debug mask. Indicates whether debug exceptions from watchpoint, breakpoint, and software step debug events that are targeted at the Exception level the exception occurred in were masked or not.
A | SError (System Error) mask bit.
I | IRQ mask bit.
F | FIQ mask bit.
M[4] | Execution state that the exception was taken from. A value of 0 indicates AArch64.
M[3:0] | Mode or Exception level that an exception was taken from.
In ARMv8, the SPSR written to depends on the Exception level. If the exception is taken in EL1, then SPSR_EL1 is used. If the exception is taken in EL2, then SPSR_EL2 is used, and if the exception is taken in EL3, SPSR_EL3 is used. The core populates the SPSR when taking an exception.

## Slide 30: Exception Levels
There’re four exception levels,
EL0 is the least privileged level, indeed it is called unprivileged execution. Apps are runned here.
EL1: for the OS kernel
EL2: provides support for virtualization of Non-secure operation. Hypervisor run in this mode
EL3 provides support for switching between two Security states, Secure state and Non-secure state. Secure monitor can be exected here.
When executing in AArch64 state, execution can move between Exception levels only on taking an exception or on returning from an exception.
Each of the 4 privilege levels has 3 private banked registers: the Exception Link Register, Stack Pointer and Saved PSR.

## Slide 31: Processor State
AArch64 does not have a direct equivalent of the ARMv7 Current Program Status Register (CPSR). In AArch64, the components of the traditional CPSR are supplied as fields that can be made accessible independently. These are referred to collectively as Processor State (PSTATE).
In AArch64, you return from an exception by executing the ERET instruction, and this causes the SPSR_ELn to be copied into PSTATE. This restores the ALU flags, execution state, Exception level, and the processor branches. From here, you continue execution from the address in ELR_ELn.
The PSTATE.{N, Z, C, V} fields can be accessed at EL0. All other PSTATE fields can be executed at EL1 or higher and are undefined at EL0.

## Slide 32: Distinguishing between 32-bit and 64-bit A64 instructions
Most integer instructions in the A64 instruction set have two forms, which operate on either 32-bit or 64-bit values within the 64-bit general-purpose register file.
When looking at the register name that the instruction uses:
If the register name starts with X, it is a 64-bit value.
If the register name starts with W, it is a 32-bit value.
Where a 32-bit instruction form is selected, the following facts hold true:
Right shifts and rotates inject at bit 31, instead of bit 63.
The condition flags, where set by the instruction, are computed from the lower 32 bits.
Writes to the W register set bits [63:32] of the X register to zero.
This distinction applies even when the results of a 32-bit instruction form would be indistinguishable from the lower 32 bits computed by the equivalent 64-bit instruction form.
For example, a 32-bit bitwise ORR could be performed using a 64-bit ORR and simply ignoring the top 32 bits of the result. The A64 instruction set includes separate 32 and 64-bit forms of the ORR instruction.

## Slide 33: Data Type in A64
Data types are simply these:
Byte: 8 bits.
Halfword: 16 bits.
Word: 32 bits.
Doubleword: 64 bits.
Quadword: 128 bits.
The architecture also supports the following floating-point data types:
Half-precision floating-point formats.
Single-precision floating-point format.
Double-precision floating-point format.

## Slide 34: Stack on A64
The stack implementation is full-descending: in a push the stack pointer is decremented, i.e the stack grows towards lower address. Another features is that stack must be quad-word aligned: SP mod 16 = 0.
A64 instructions can use the stack pointer only in a limited number of cases:
Load/Store instructions use the current stack pointer as the base address: When stack alignment checking is enabled by system software and the base register is SP, the current stack pointer must be initially quadword aligned, That is, it must be aligned to 16 bytes. Misalignment generates a Stack Alignment fault.
Add and subtract data processing instructions in their immediate and extended register forms, use the current stack pointer as a source register or the destination register or both.
Logical data processing instructions in their immediate form use the current stack pointer as the destination register.

## Slide 35: Condition Code Suffixes on A64
Suffix | Flags | Meaning
EQ | Z set | Equal
NE | Z clear | Not equal
CS or HS | C set | Higher or same (unsigned >= )
CC or LO | C clear | Lower (unsigned < )
MI | N set | Negative
PL | N clear | Positive or zero
VS | V set | Overflow
VC | V clear | No overflow
HI | C set and Z clear | Higher (unsigned >)
LS | C clear or Z set | Lower or same (unsigned <=)
GE | N and V the same | Signed >=
LT | N and V differ | Signed <
GT | Z clear, N and V the same | Signed >
LE | Z set, N and V differ | Signed <=
AL | Any | Always. This suffix is normally omitted.

## Slide 36
Load and Store on A64
There’re many instructions in this class to move many data size: byte, halfword and word, but I show only four, just to make you understand them : two for move single register and two for move a pair of registers;
=
Load/Store addressing modes
This part is very important to understand different ARM addressing modes; the most used are three:
[base{, #imm}]: Base plus offset addressing means that the address is the value in the 64-bit base register plus an offset.
  Example: ldrsw x0, [x29,76] #load signed word in x0
[base, #imm]! : Pre-indexed addressing means that the address is the sum of the value in the 64-bit base register and an offset, and the address is then writtenback to the base register.
  Example: stp x29, x30, [sp, -80]! #store x9 e x30 into stack from sp-80
[base], #imm : Post-indexed addressing means that the address is the value in the 64-bit base register, and the sum of the address and the offset is then written back to the base register.
  Example: ldp x29, x30, [sp], 80 #load values from stack

## Slide 37: Single Register
Single Register Save a register into a memory
ldr: Load register works with:
  Register offset: LDR <Xt>, [<Xn|SP>, <R><m>{, <extend> {<amount>}}]
  Immediate offset: LDR <Xt>, [<Xn|SP>], #<simm>
  PC-relative literal: LDR <Xt>, <label
str: Store register:
  register offset: STR <Xt>, [<Xn|SP>, <R><m>{, <extend> {<amount>}}]
  immediate offset: STR <Xt>, [<Xn|SP>], #<simm>
<simm> is signed immediate byte offset, in the range -256 to 255

## Slide 38: Store and Load a pair of registers
Save the two registers specified into memory address of Xn or SP
ldp load pair: LDP <Xt1>, <Xt2>, [<Xn|SP>], #<imm>
stp store pair: STP <Xt1>, <Xt2>, [<Xn|SP>], #<imm>
<imm> is signed immediate byte offset, a multiple of 8 in the range -512 to 504

## Slide 39: Data processing -Arithmetic
ADD | ADD (immediate) | ADD <Xd¦SP>, <Xn¦SP>, #<imm>{, <shift>}; Rd = Rn + shift(imm)
ADDS | Add and set flags | 
SUB | Subtract | SUB <Xd¦SP>, <Xn¦SP>, #<imm>{, <shift>}; Rd = Rn – shift(imm)
SUBS | Subtract and set flags | 
CMP | Compare | CMP <Xn¦SP>, #<imm>{, <shift>}
CMN | Compare negative | 

## Slide 40: Data processing - Logical
AND | Bitwise | AND <Xd¦SP>, <Xn>, #<imm> ;Rd = Rn AND imm
ANDS | Bitwise AND and set flags | ANDS <Xd>, <Xn>, #<imm> ;Rd = Rn AND imm
EOR | Bitwise exclusive | EOR <Xd¦SP>, <Xn>, #<imm> ;Rd = Rn EOR imm
ORR | Bitwise inclusive | ORR <Xd¦SP>, <Xn>, #<imm> ;Rd = Rn OR imm
TST | Test bits | TST <Xn>, #<imm> ;Rn AND imm

## Slide 41: Move Instruction
MOVZ | Move wide with zero | MOVZ <Xd>, #<imm>{, LSL #<shift>} ;Rd = LSL (imm16, shift)
MOVN | Move wide with NOT | MOVN <Xd>, #<imm>{, LSL #<shift>} ;Rd = NOT (LSL (imm16, shift))
MOVK | Move 16-bit immediate into register, keeping other bits unchange | MOVK <Xd>, #<imm>{, LSL #<shift>} ; Rd<shift+15:shift> = imm16

## Slide 42: PC-relative address calculation
The ADR instruction adds a signed, 21-bit immediate to the value of the program counter that fetched this instruction, and then writes the result to a general-purpose register: ADR <Xd>, <label>
The ADRP instruction permits the calculation of the address at a 4KB aligned memory region. In conjunction with an ADD(immediate) instruction, or a Load/Store instruction with a 12-bit immediate offset, this allows for the calculation of, or access to, any address within ±4GB of the current PC: ADRP <Xd>, <label

## Slide 43: Shift Operation
ASR | Arithmetic shift right | ASR <Xd>, <Xn>, #<bits to shift>
LSL | Logical shift left | LSL <Xd>, <Xn>, #<shift>
LSR | Logical shift right | LSR <Xd>, <Xn>, #<shift>
ROR | Rotate right | ROR <Xd>, <Xs>, #<bits to shift>

## Slide 44: Arithmetic Shifted Register
ADD: Add
ADDS: Add and set setting the condition flags
SUB: Subtract
SUBS: Subtract and set flags
CMN: Compare negative
CMP: Compare
NEG: Negate ; Rd = 0 – shift(Rm, amount)
NEGS: Negate and set flags
How ADD works, the others are similar: ADD <Xd>, <Xn>, <Xm>{, <shift> #<amount>} Rd = Rn + shift(Rm, amount);

## Slide 45: Arithmetic with carry
ADC: Add with carry ADC <Xd>, <Xn>, <Xm>
ADCS: Add with carry and set flags ADCS <Xd>, <Xn>, <Xm> ;Rd = Rn + Rm + C
SBC: Subtract with carry SBC <Xd>, <Xn>, <Xm> ;Rd = Rn – Rm – 1 + C
SBCS: Subtract with carry and set flags
NGC: Negate with carry NGC <Xd>, <Xm> ;Rd = 0 – Rm – 1 + C
NGCS: Negate with carry and set flags

## Slide 46: Data Processing
MADD Multiply-add MADD <Xd>, <Xn>, <Xm>, <Xa>; Rd = Ra + Rn * Rm
MSUB Multiply-subtract
MNEG Multiply-negate
MUL Multiply MUL <Xd>, <Xn>, <Xm>; Rd = Rn * Rm
SMADDL Signed multiply-add long
SMSUBL Signed multiply-subtract long
SMNEGL Signed multiply-negate long
SMULL Signed multiply long
SMULH Signed multiply high
UMADDL Unsigned multiply-add long
UMSUBL Unsigned multiply-subtract long
UMNEGL Unsigned multiply-negate long
UMULL Unsigned multiply long
UMULH Unsigned multiply high
SDIV Signed divide SDIV <Xd>, <Xn>, <Xm>; Rd = Rn / Rm
UDIV Unsigned divide

## Slide 47: Conditional Select
CSEL | Conditional select | CSEL <Xd>, <Xn>, <Xm>, <cond> ;Rd = if cond then Rn else Rm
CSINC | Conditional select increment | CSINC <Xd>, <Xn>, <Xm>, <cond> ;Rd = if cond then Rn else (Rm
 |  | + 1)
CSINV | Conditional select inversion | CSINV <Xd>, <Xn>, <Xm>, <cond> ;Rd = if cond then Rn else NOT (Rm)
CSNEG | Conditional select negation | CSNEG <Xd>, <Xn>, <Xm>, <cond> ;Rd = if cond then Rn else -Rm
CSET | Conditional set | CSET <Xd>, <cond> ;Rd = if cond then 1 else 0
CSETM | Conditional set mask | CSETM <Xd>, <cond> ;Rd = if cond then -1 else 0
CINC | Conditional increment | CINC <Xd>, <Xn>, <cond> ;Rd = if cond then Rn+1 else Rn
CINV | Conditional invert | CINV <Xd>, <Xn>, <cond> ;Rd = if cond then NOT(Rn) else Rn
CNEG | Conditional negate | CNEG <Xd>, <Xn>, <cond> ;Rd = if cond then -Rn else Rn
The Conditional select instructions select between the first or second source register, depending on the current state of the condition flag

## Slide 48: Conditional comparison
The Conditional comparison instructions provide a conditional select for the NZCV condition flags, setting the flags to the result of an arithmetic comparison of its two source register values if the named input condition is true, or to an immediate value if the input condition is false. There are register and immediate forms. The immediate form compares the source register to a small 5-bit unsigned value.
CCMN | Conditional compare negative (register) | CCMN <Xn>, <Xm>, #<nzcv>, <cond> ;flags = if cond then compare(Rn, -Rm) else #nzcv
CCMN | Conditional compare negative (immediate) | CCMN <Xn>, #<imm>, #<nzcv>, <cond> ;flags = if cond then compare(Rn, #-imm) else #nzcv
CCMP | Conditional compare (register) | CCMP <Xn>, <Xm>, #<nzcv>, <cond> ;flags = if cond then compare(Rn, Rm) else #nzcv
CCMP | Conditional compare (immediate) | CCMP <Xn>, #<imm>, #<nzcv>, <cond> ;flags = if cond then compare(Rn, #imm) else #nzcv