## Slide 1: Cortex M4
Girish S Kumar
Notes: Click to add notes

## Slide 2: Cortex- M4 Architecture
General Overview of Cortex- M4
Some Features of Cortex M4
Physical Design Details
Cortex M4 Block Diagram
Programmer View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.

## Slide 3: Cortex M4 General View
Cortex-M4 Processor
  Introduced in 2010
  Designed with a large variety of highly efficient signal processing features
  Features extended single-cycle multiply accumulate instructions, optimized SIMD arithmetic, saturating arithmetic and an optional Floating Point Unit.
High Performance Efficiency
  1.25 DMIPS/MHz (Dhrystone Million Instructions Per Second / MHz) at the order of µWatts / MHz
Low Power Consumption
  Longer battery life – especially critical in mobile products
Enhanced Determinism
  The critical tasks and interrupt routines can be served quickly in a known number of cycles

## Slide 4: General Overview
32-bit Reduced Instruction Set Computing (RISC) processor
Harvard architecture
  Separated data bus and instruction bus
Instruction set
  Include the entire Thumb®-1 (16-bit) and Thumb®-2 (16/ 32-bit) instruction sets
3-stage + branch speculation pipeline
Performance efficiency
  1.25 – 1.95 DMIPS/MHz (Dhrystone Million Instructions Per Second / MHz)
Supported Interrupts
  Non-maskable Interrupt (NMI) + 1 to 240 physical interrupts
  8 to 256 interrupt priority levels

## Slide 5: Features
Supports Sleep Modes
  Up to 240 Wake-up Interrupts
  Integrated WFI (Wait For Interrupt) and WFE (Wait For Event) Instructions and Sleep On Exit capability (to be covered in more detail later)
  Sleep & Deep Sleep Signals
  Optional Retention Mode with ARM Power Management Kit
Enhanced Instructions
  Hardware Divide (2-12 Cycles)
  Single-Cycle 16, 32-bit MAC, Single-cycle dual 16-bit MAC
  8, 16-bit SIMD arithmetic
Debug
  Optional JTAG & Serial-Wire Debug (SWD) Ports
  Up to 8 Breakpoints and 4 Watchpoints
Memory Protection Unit (MPU)
  Optional 8 region MPU with sub regions and background region

## Slide 6: Physical design details
Cortex-M4 processor is designed to meet the challenges of low dynamic power constraints while retaining light footprints
  180 nm ultra low power process –157 µW/MHz
  90 nm low power process – 33 µW/MHz
  40 nm General process – 8 µW/MHz
ARM Cortex-M4 Implementation Data |  |  | 
Process | 180ULL (7-track, typical 1.8v, 25C) | 90LP (7-track, typical 1.2v, 25C) | 40G 9-track, typical 0.9v, 25C)
Dynamic Power | 157 µW/MHz | 33 µW/MHz | 8 µW/MHz
Floorplanned Area | 0.56 mm2 | 0.17 mm2 | 0.04 mm2

## Slide 7: What are the goals of design
A 32 Bit microcontroller
It is designed to achieve
    High code density,
    Fast interrupt response times
    Signal processing Algorithms
    IEEE floating-point units
    Real time Operating System support
    Advance Trace Capabilities
Notes:   How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
  Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 8: Cortex-M4 Details
A 32 Bit microcontroller
Can handle 32 bit, 16 bit and 8 –bit data effectively
Cortex-M4 does not include any memory but provides interfaces to external Flash and SRAMs
32 bit address bus lets us address 4GB of Memory
Different regions are created memory space to store system instructions and data, users instructions, data, and mapped peripheral device registers and related interfaces.
Cortex -M4 internally uses a 32 But bus based on AMBA standard, Advanced Microcontroller Bus Architecture
The main bus interface between the MCU and external components is the Advanced High performance Bus (AHB), which provides interfaces for memory and system bus as well as for peripheral devices

## Slide 9: Cortex-M4 Block Diagram
Optional
WIC
Nested Vector
Interrupt
Controller
(NVIC)
Optional
Debug
Access Port
ARM Cortex-M4 Microprocessor
Optional Memory
protection unit
Bus matrix
Code interface
SRAM and
peripheral interface
Optional FPU
Processor core
Optional
Embedded
Trace Macrocell
Optional Serial
Wire Viewer
Optional
Flash
patch
Optional
Data
watchpoints

## Slide 10
Cortex-M4 Block Diagram
Processor core
  Contains internal registers, the ALU, data path, and some control logic
  Registers include sixteen 32-bit registers for both general and special usage
Processor pipeline stages
  Three-stage pipeline: fetch, decode, and execution
  Some instructions may take multiple cycles to execute, in which case the pipeline will be stalled
  The pipeline will be flushed if a branch instruction is executed
  Up to two instructions can be fetched in one transfer (16-bit instructions)
  .
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Instruction 1
Instruction 2
Instruction 3
Fetch
Decode
Execute
Instruction 4
Time

## Slide 11
Cortex-M4 Block Diagram
Processor core
  Contains internal registers, the ALU, data path, and some control logic
  Registers include sixteen 32-bit registers for both general and special usage
Processor pipeline stages
  Three-stage pipeline: fetch, decode, and execution
  Some instructions may take multiple cycles to execute, in which case the pipeline will be stalled
  The pipeline will be flushed if a branch instruction is executed
  Up to two instructions can be fetched in one transfer (16-bit instructions)
  an instruction can be fetched several cycles ahead of the decode and execution stages.

## Slide 12
Cortex-M4 Block Diagram
Nested Vectored Interrupt Controller (NVIC)
  Up to 240 interrupt request signals and a non-maskable interrupt (NMI)
  Automatically handles nested interrupts, such as comparing priorities between interrupt requests and the current priority level
Wakeup Interrupt Controller (WIC)
  For low-power applications, the microcontroller can enter sleep mode by shutting down most of the components.
  When an interrupt request is detected, the WIC can inform the power management unit to power up the system.
Memory Protection Unit (optional)
  Used for protecting memory content, e.g. make some memory regions read-only or preventing user applications from accessing privileged application data

## Slide 13
Cortex-M4 Block Diagram
Bus interconnect
  Allows data transfer to take place on different buses simultaneously
  Provides data transfer management, e.g. a write buffer, bit-oriented operations (bit-band)
  May include bus bridges (e.g. AHB-to-APB bus bridge) to connect different buses into a network using a single global memory space
  Includes the internal bus system, the data path in the processor core, and the AHB LITE interface unit
Debug subsystem
  Handles debug control, program breakpoints, and data watchpoints
  When a debug event occurs, it can put the processor core in a halted state, where developers can analyse the status of the processor at that point, such as register values and flags

## Slide 14: Cortex M4 - Architecture
General Overview of Cortex- M4
Some Features
Physical Design Details
Cortex M4 Block Diagram
Programmers View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.

## Slide 15
Programmers View

## Slide 16
Processor Modes
Cortex –M4 has two modes
Thread Mode
Handler mode
Processor Mode | What happens in this mode
Thread mode | All User Application executes in this mode, when processor is RESET and completes the reset process, it automatically comes to Thread mode
Handler mode | All Exceptions are handled in this mode, once the exception handling is completed it goes back to thread mode

## Slide 17: Privileges in Mode
 | Privilege Mode | What can a program do in the mode
1 | Privileged mode | No Restrictions – Full access to everything
2 | Unprivileged mode | A program in this mode has limited access the xPSR register or it flags through MRS and MSR instructions Cannot access system timer, Nested Vectored Interrupt Controller (NVIC) , system control block May have restricted access to memory or peripherals.
Notes: Lesson descriptions should be brief.

## Slide 18: Processor Mode and Privileges
Use of this mode:
Exception Handling
Stack : Main
Use of this mode:
Applications use this mode
Under special conditions
Stack : Main or process
Use of this mode:
Applications will be in this mode most of the time
Stack : Main or process
Handler
mode
Thread
mode
Privileged
User
Privileged
User
Thread
mode
Processor mode
Privileges
Notes: Example objectives
At the end of this lesson, you will be able to:
  Save files to the team Web server.
  Move files to different locations on the team Web server.
  Share files on the team Web server.

## Slide 19: Registers in Cortex-M4

## Slide 20
Processor registers
  The internal registers are used to store and process temporary data within the processor core
  All registers are inside the processor core, hence they can be accessed quickly
  Load-store architecture
          To process memory data, they have to be first loaded from memory to registers, processed inside the processor core using register data only, and then written back to memory if needed
Cortex-M4 registers
  Register bank
          Sixteen 32-bit registers (thirteen are used for general-purpose);
  Special registers
Cortex-M4 Registers

## Slide 21
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(SP)
R14 (LR)
R15(PC)
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
MSP
PSP
Banked Version
General
Purpose
Registers
Low Registers
High Registers
Program Status Register
Control Register
Exception Register
Special Purpose Registers

## Slide 22
R0 – R12: general purpose registers
  Low registers (R0 – R7) can be accessed by any instruction
  High registers (R8 – R12) sometimes cannot be accessed e.g. by some Thumb (16-bit) instructions
R13: Stack Pointer (SP)
  Records the current address of the stack
  Used for saving the context of a program while switching between tasks
  Cortex-M4 has two SPs: Main SP, used in applications that require privileged access e.g. OS kernel, and exception handlers, and Process SP, used in base-level application code (when not running an exception handler)
Program Counter (PC)
  Records the address of the current instruction code
  Automatically incremented by 4 at each operation (for 32-bit instruction code), except branching operations
  A branching operation, such as function calls, will change the PC to a specific address, meanwhile it saves the current PC to the Link Register (LR)
Cortex-M4 Registers

## Slide 23
Cortex-M4 Registers
R14: Link Register (LR)
  The LR is used to store the return address of a subroutine or a function call
  The program counter (PC) will load the value from LR after a function is finished
PC
LR
Main
Program
code
subroutine
Current PC
Load PC with the address in LR to return to the main program
Current LR
Return from a subroutine to the main program
PC
LR
Main
Program
code
subroutine
Current PC
1. Save current
PC to LR
2. Load PC with the starting address of the subroutine
Call a subroutine
Code region
Code region

## Slide 24: Stacks in ARM processor

## Slide 25: Types of Stack
Ascending Stack:
In a push the stack pointer is incremented, i.e the stack grows towards higher address.
Descending Stack:
In a push the stack pointer is decremented, i.e the stack grows towards lower address.
Ascending Empty stack
Stack pointer points to the location in which the next item will be stored. A push will store the value, and increment the stack pointer.
Ascending Full Stack
Stack pointer points to the location in which the last item was stored. A push will increment the stack pointer and store the value.
Descending Empty stack
Stack pointer points to the location in which the next item will be stored. A push will store the value, and increment the stack pointer.
Full stack
Descending Full Stack
Stack pointer points to the location in which the last item was stored. A push will increment the stack pointer and store the value

## Slide 26
The Cortex M4 uses a full descending stack. This means the stack pointer holds the
address of the last stacked item in memory.
The processor implements two stacks, the main stack and the process stack, with a pointer for each held in independent registers,
Stack on Cortex M4
Processor Mode | Used to execute | Privilege level | STACK USED
Thread | Applications | Privileged or Un privileged | Process stack or Main stack Based on CONTROL Register
Handler | Exceptions | Always Privileged | Main Stack
R13(SP)
MSP
PSP
Main Stack
Process stack

## Slide 27
CONTROL Register
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The CONTROL is a 32 bit register, that controls the
Which stack used at a given time
When the processor is in Thread mode it decides the privilege level
Indicates whether the Floating point Unit is active
BITS | Name | Function
31 …… 3 Bits | No name | Reserved
2 | FPCA | 0 = no floating-point context active 1 = floating-point context active.
1 | SPSEL | 0 = MSP is the current stack pointer 1 = PSP is the current stack pointer.
0 | nPRIV | Defines the Thread mode privilege level: 0 = privileged 1 = unprivileged.

## Slide 28
Program Status Register (PSR) Cortex M4
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 20 | 19 | 16 | 15 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
N | Z | C | V | Q |  |  |  |  |  | G.. | ..E |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | ICI/IT |  | T |  |  |  | ICI/IT |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ISR NUMBER |  |  |  |  |  |  | 
APSR
EPSR
IPSR
4 Bits

## Slide 29
The APSR contains the status flags (N, C, V, and Z), the Greater Than or Equal flags (used by the SEL instruction), and an additional “sticky” Q flag used in saturation arithmetic, where sticky in this case means that the bit can only be cleared by explicitly writing a zero to it.
BITS | NAME | FUNCTION
31 | N | Negative Flag
30 | Z | Zero Flag
29 | C | Carry or Borrow Flag
28 | V | Overflow Flag
27 | Q | DSP Overflow and Saturation Flag
26:20 | - | Reserved
19:16 | GE[3:0] | Greater than or Equal flags for SEL instruction
15:0 | - | Reserved
APSR Bit assignments
Application Program Status Register (APSR),

## Slide 30
SEL Instruction
The SEL instruction:
1. Reads the value of each bit of APSR.GE.
2. Depending on the value of APSR.GE, assigns the destination register the value of
either the first or second operand register.
Examples
SADD16 R0, R1, R2 ; Set GE bits based on result
SEL R1, R0, R3 ; Select bytes from R0 or R3 and assign to to R1, based on GE.

## Slide 31
IPSR contains only an exception number that is used in handling faults and other types of exceptions.
Interrupt Program Status Register (IPSR)
BITS | NAME | FUNCTION
[31:9] | - | Reserved
[8:0] | ISR NUMBER | This is the number of the current exception: 0 = Thread mode 1 = Reserved 2 = NMI 3 = HardFault 4 = MemManage 5 = BusFault 6 = UsageFault 7-10 = Reserved 11 = SVCall 12 = Reserved for Debug 13 = Reserved 14 = PendSV 15 = SysTick 16 = IRQ0. . . . n+15 = IRQ(n-1)a

## Slide 32
Two fields contain the IF-THEN instruction status bits overlapped with the
Interrupt-Continuable Instruction (ICI) bits, PLUS the Thumb (T) bit
Execution Program Status Register (EPSR)
BITS | NAME | FUNCTION
[31:27] | - | Reserved
[26:25], [15:10] | ICI | Interruptible-continuable instruction bits
[26:25], [15:10] | IT | Indicates the execution state bits of the IT instruction. (To be discussed Later)
[24] | T | Thumb state bit. (To be discussed Later)
[23:16] | - | Reserved
[9:0] | - | Reserved

## Slide 33
When an interrupt occurs during the execution of an LDM, STM, PUSH, or POP instruction, and when
an FPU is implemented an VLDM, VSTM, VPUSH, or VPOP instruction, the processor:
• stops the load multiple or store multiple instruction operation temporarily
• stores the next register operand in the multiple operation to EPSR bits[15:12].
After servicing the interrupt, the processor:
• returns to the register pointed to by bits[15:12]
• resumes execution of the multiple load or store instruction.
When the EPSR holds ICI execution state, bits[26:25,11:10] are zero.
What are Interruptible-continuable instructions

## Slide 34
Exception Registers Cortex M4
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL

## Slide 35: PRIMASK
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The PRIMASK register prevents activation of all exceptions with configurable priority.
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | PRIMASK | 0 = no effect 1 = prevents the activation of all exceptions with configurable priority

## Slide 36: FAULT MASK
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The FAULTMASK register prevents activation of all exceptions except for Non-Maskable Interrupt (NMI).
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | FAULTMASK | 0 = no effect 1 = prevents the activation of all exceptions except for NMI.

## Slide 37
BASEPRI
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The BASEPRI register defines the minimum priority for exception processing. When BASEPRI is set to a nonzero value, it prevents the activation of all exceptions with the same or lower priority level as the BASEPRI value
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | FAULTMASK | Priority mask bits: 0x00 = no effect Nonzero = defines the base priority for exception processing. The processor does not process any exception with a priority value greater than or equal to BASEPRI.

## Slide 38
Cortex-M4 Registers
Reserved
Reserved
BASEPRI
BASEPRI
CONTROL
bit8
bit16
bit24
bit31
Stack definition
Reserved
FAULTMASK
FAULTMASK
Reserved
PRIMASK
PRIMASK

## Slide 39
Register Summary
Name | Type | Required Privilege
[R0-R12] | RW | Either
MSP | RW | Privileged
PSP | RW | Either
LR | RW | Either
PC | RW | Either
PSR | RW | Privileged
APSR | RW | Either
IPSR | RO | Privileged
EPSR | RO | Privileged
PRIMASK | RW | Privileged
FAULTMASK | RW | Privileged
BASEPRI | RW | Privileged
CONTROL | RW | Privileged

## Slide 40
What is IEEE Single Precision and Double Precision ?
The IEEE single precision floating point standard representation requires a 32 bit word
which may be represented as numbered from 0 to 31, left to right.
The 0th is the sign bit, S,
the next eight bits [1:8] are the exponent bits, 'E', and
the final 23 bits are the fraction 'F':
The IEEE double precision floating point standard representation requires a 64 bit word
which may be represented as numbered from 0 to 63, left to right.
The first bit is the sign bit, S,
The next eleven bits are the exponent bits, 'E', and
The final 52 bits are the fraction 'F':

## Slide 41
Floating Point Processing
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(SP)
R14 (LR)
R15(PC)
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
MSP
PSP
Banked Version
General
Purpose
Registers
Low Registers
High Registers
Program Status Register
Control Register
Exception Register
Special Purpose Registers
32 single-precision floating-point registers (s0–s31) or 16 double-precision
registers (d0–d15) or a mix
S0
S1
S2
S3
S30
S31
D0
D1
D15

## Slide 42
Cortex M4 - Architecture
General Overview of Cortex- M4
Some Features
Physical Design Details
Cortex M4 Block Diagram
Programmers View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.