## Slide 1
Cortex M4 - Architecture
General Overview of Cortex- M4
Some Features
Physical Design Details
Cortex M4 Block Diagram
Programmers View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.

## Slide 2
Memory Architecture

## Slide 3: Memory Architecture
The maximum searchable memory capacity in the Cortex -M4 system can be up to
4 GB. The bus interface between the MCU and external memory is the
Advanced High-performance Bus (AHB), which provides interfaces and connections to
various 32/16/8-bit memory devices.
To make memory access more effective the entire 4GB memory space is divided into
the different regions with the help of the multiple bus interfaces processor that can access
different memory regions, such as from the CODE region stored program codes to
DATA region in the SRAM or peripheral regions, simultaneously or at the same time
In the ARM Cortex-M4 MCU, an optional unit, Memory Protection Unit (MPU), is
provided to enable users to access different memory regions with certain permissions. The MPU is a programmable unit that defines access permissions for different regions. The MPU supports eight programmable regions. (Implementation Specific)

## Slide 4
Cortex-M4 Memory Map
The Cortex-M4 processor has 4 GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined as a number of regions
  Each region is given for recommended usage
  Easy for software programmer to port between different devices
Nevertheless, despite of the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus

## Slide 5
Cortex-M4 Memory Map
Private peripherals
e.g. NVIC, SCS
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH
Vendor specific
Memory
External device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
(PPB)
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM table
External PPB
Embedded trace macrocell
Trace port interface unit
Reserved
System Control Space, including
Nested Vectored Interrupt
Controller (NVIC)
Reserved
Fetch patch and breakpoint unit
Data watchpoint and trace unit
Instrumentation trace macrocell
External PPB
Internal PPB

## Slide 6
Cortex-M4 Memory Map
Code Region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM Region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM or other types
Peripheral Region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals
  On-chip peripherals

## Slide 7
Cortex-M4 Memory Map
External RAM Region
  Primarily used to store large data blocks, or memory caches
  Off-chip memory, slower than on-chip SRAM region
External Device Region
  Primarily used to map to external devices
  Off-chip devices, such as SD card
Internal Private Peripheral Bus (PPB)
  Used inside the processor core for internal control
  Within PPB, a special range of memory is defined as System Control Space (SCS)
  The Nested Vectored Interrupt Controller (NVIC) is part of SCS

## Slide 8
Cortex-M4 Memory Map Example
AHB bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M4
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon

## Slide 9
Bit-band Operations
Bit-band operation allows a single load/store operation to access a single bit in the memory, for example, to change a single bit of one 32-bit data:
  Normal operation without bit-band (read-modify-write)
          Read the value of 32-bit data
          Modify a single bit of the 32-bit value (keep other bits unchanged)
          Write the value back to the address
  Bit-band operation
          Directly write a single bit (0 or 1) to the “bit-band alias address” of the data
Bit-band alias address
  Each bit-band alias address is mapped to a real data address
  When writing to the bit-band alias address, only a single bit of the data will be changed

## Slide 10
Bit-band Operation Example
For example, in order to set bit[3] in word data in address 0x20000000:
Read-Modify-Write operation
  Read the real data address (0x20000000)
  Modify the desired bit (retain other bits unchanged)
  Write the modified data back
Bit-band operation
  Directly set the bit by writing ‘1’ to address 0x2200000C, which is the alias address of the fourth bit of the 32-bit data at 0x20000000
          In effect, this single instruction is mapped to 2 bus transfers: read data from 0x20000000 to the buffer, and then write to 0x20000000 from the buffer with bit [3] set
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read
ORR.W R0, #0x8 ;Modify bit
STR R0, [R1] ;Write back
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write

## Slide 11
Bit-band Alias Address
Each bit of the 32-bit data is one-to-one mapped to the bit-band alias address
  For example, the fourth bit (bit [3]) of the data at 0x20000000 is mapped to the bit-band alias address at 0x2200000C
  Hence, to set bit [3] of the data at 0x20000000, we only need to write ‘1’ to address 0x2200000C
  In Cortex-M4, there are two pre-defined bit-band alias regions: one for SRAM region, and one for peripherals region
0x20000000
0x20000004
0x20000008
Real 32-bit data address
0x22000000
0x22000080
0x22000100
0x2200000C
0x22000018
Bit-band alias address

## Slide 12
Bit-band Alias Address
SRAM region
  32MB memory space (0x22000000 – 0x23FFFFFF) is used as the bit-band alias region for 1MB data (0x20000000 – 0x200FFFFF)
Peripherals region
  32MB memory space (0x42000000 – 0x43FFFFFF) is used as the bit-band alias region for 1MB data (0x40000000 – 0x400FFFFF)
External RAM
Peripherals
SRAM
Code
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x20000000
0x20100000
0x22000000
0x23FFFFFF
0x21FFFFFF
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x40000000
0x40100000
0x42000000
0x43FFFFFF
0x41FFFFFF

## Slide 13
Benefits of Bit-Band Operations
Faster bit operations
Fewer instructions
Atomic operation, avoid hazards
  For example, if an interrupt is triggered and served during the Read-Modify-Write operations, and the interrupt service routine modifies the same data, a data conflict will occur
Interrupt Service Routine
Interrupt occurs
Read data at 0x00
Modify bit [1]
Read data at 0x00
Modify bit [1]
Write data back
Write data back
Interrupt returns
Bit [1] modified by ISR is overwritten
by the main program
Main program

## Slide 14
Cortex-M4 Program Image
The program image in Cortex-M4 contains
  Vector table -- includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP);
  C start-up routine;
  Program code – application code and data;
  C library code – program codes for C library functions.
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Initial MSP value
Reset vector
NMI vector
Hard fault vector
MemManage fault
Reserved
PendSV
SysTick
External Interrupts
Bus fault
Usage fault
Reserved
SVCall
Debug monitor

## Slide 15
Cortex-M4 Program Image
After Reset, the processor:
  First reads the initial MSP value;
  Then reads the reset vector;
  Branches to the start of the programme execution address (reset handler);
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)

## Slide 16
Cortex-M4 Endianness
Endian refers to the order of bytes stored in memory
  Big endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M4 supports both little endian and big endian
However, Endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory

## Slide 17
Cortex M4 - Architecture
General Overview of Cortex- M4
Some Features
Physical Design Details
Cortex M4 Block Diagram
Programmers View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.

## Slide 18
Nested Vectored Interrupt Control.

## Slide 19: Nested Vectored Interrupt Control.
The Nested Vectored Interrupt Controller (NVIC is used to handle and pre-process all exceptions and interrupts, including makeable and unmask able interrupts,
An exception or interrupt is first created by an interrupt source and sent to processor
Based on the mask register’s content and the interrupt priority level, CPU will
determine whether to response or process the interrupt request.
If the interrupt request is accepted, the associated hardware will provide
interrupt related information, such as the interrupt source and related Interrupt
Service Routine (ISR) entry point, in a Vector Table format.
4. Before the control can be transferred to the ISR, all related registers are pushed
into the stack to reserve their contents
5. Then the control will be directed to the entry point (entry address of the ISR) to
run the ISR to perform the required interrupt service.

## Slide 20: Nested Vectored Interrupt Control.
5. After the ISR is done and before the control can be transferred back to the main Program
6. All related registers pushed on to start , including the PC, are recovered by popping them back to the related registers
7. Then the control can be directed to the main program to continue executing the normal application codes based on the old PC content.

## Slide 21: Vector Table
The Cortex-M4 vector table is probably one of the larger departures from all previous ARM processor designs. Returning to the idea that addresses are stored in the vector table, rather than instructions,
Exception Type | Exception No | Address
(Top of Stack) | ------------ | 0x00000000
Reset | 1 | 0x00000004
NMI | 2 | 0x00000008
Hard Fault | 3 | 0x0000000C
Memory management fault | 4 | 0x00000010
Bus Fault | 5 | 0x00000014
Usage Fault | 6 | 0x00000018
SV Call | 11 | 0x0000002c
Debug monitor | 12 | 0x00000030
Pend SV | 14 | 0x00000038
Sys Tick | 15 | 0x0000003c
Interrupts | 16 and above | 0x00000040 and above

## Slide 22: Nested interrupt vector Controller
The NVIC supports nesting (stacking) of interrupts, allowing an interrupt to be
serviced earlier by exerting higher priority. It also supports dynamic reprioritisation
of interrupts. Priority levels can be changed by software during run time. Interrupts
that are being serviced are blocked from further activation until the interrupt service
routine is completed, so their priority can be changed without risk of accidental
re-entry.

## Slide 23
Cortex M4 - Architecture
Programmer View
Memory architecture.
Nested Vectored Interrupt Control.
Debug architecture.

## Slide 24: Debug Architecture
In theARM Cortex-M4 system, two types of interfaces to understand
“WHAT IS HAPPENING INSIDE”
  Debug
  Trace.
The debug interface to perform the debug functions,
Run Control of the processor allowing you to start and stop programs
Single Step one source or assembler line
Set breakpoints while the processor is running
Read/write memory contents and peripheral registers on-the-fly
Program internal and external Flash memory
The trace interface is to collect dynamic information from the CPU as the
system is running,
Data,
Event,
profiling or complete details of a user’s application program.

## Slide 25
All Cortex-M3 and Cortex-M4 devices provide data and event trace.
Trace Window - Displays program flow by capturing timestamps, PC samples, exceptions, and Read/Write accesses.
Debug Viewer - Displays the printf-style output of the Instrumented Trace (ITM) in a terminal window.
Exceptions window - Displays statistical information about program exceptions and interrupts.
Event Counters - Display real-time values of specific event counters providing performance indications.
Logic Analyzer - Graphically displays variable changes in captured data trace.
RTX Event Viewer - display RTX Kernel task switching events and statistics on a time scale.
KEIL Real-Time Trace and Analysis

## Slide 26
Useful Resources
Architecture Reference Manual:
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi0403c/index.html
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf
http://stackoverflow.com/questions/801117/whats-the-difference-between-a-single-precision-and-double-precision-floating-p\
NIVC :http://wiki.csie.ncku.edu.tw/embedded/arm-exceptions.pdf